## Slide 1: Crane Aerospace & Electronics
TI digital design seminar de-brief
November 2013

## Slide 2: Analog versus digital
 | Analog | Digital
control bandwidth | high | limited by sampling
cost | historically low | getting cheaper
available expertise | high | low
flexibility | hardware based-inflexible | S/W programmable
lifetime operation | component drift/aging/tol | relatively insensitive
scalability | limited practical topologies due to complexity | low complexity cost when scaling
numerical problem | none | architecture dependent
switching frequency | very high | limited to system clock
Reliability | Military Grade Available | Military Grade Available
Rad Hard | Well tested | Limited testing

## Slide 3: Why go digital?
Easy to scale existing design through software
Less sensitive to environmental changes
Saves space for more complex converters

## Slide 4: Why TI’s C2000
Large support community
It’s cheap
High-Resolution PWM
Small form factor

## Slide 5: How cheap
Device Series | CPU Speed | Memory | Architecture Features | Starting Price
Piccolo F2806x | 90 MHz | 128kB to 256kB | Floating-point, VCU*,CLA*,DMA | $4.95
Piccolo F2805x | 60 MHz | 64kB to 128kB | Fixed-point, CLA, PGAs, Windowed Comparators | $3.25
Piccolo F2803x | 60 MHz | 64kB to 128 kB | Fixed-point, CLA* | $2.79
Piccolo F2802x | 40-60 MHz | 16kB to 64 kB | Fixed-point | $1.85

## Slide 6: Why high resolution PWM matter
Basic digital PWM (counter based)
High Res PWM

## Slide 7: Will it fit
TMS320F2803 (S-PVQFN-N56)
Replacement area
 | SMTR | 
 | qty | area (in2)
LM119 | 1 | 0.005
MC35072 | 1 | 0.005
0402 res | 30 | 0.026
0504 cap | 11 | 0.022
1N4148 | 11 | 0.003
LM158 | 1 | 0.003
 |  | 0.064
 | MFX | 
 | qty | area (in2)
UCC2897A | 1 | 0.027
TLC2272Y | 1 | 0.0038
0402 res | 25 | 0.02
0402 cap | 3 | 0.0024
0603 cap | 7 | 0.013
1N4148 | 6 | 0.0016
2N2907A | 5 | 0.0024
 |  | 0.070

## Slide 8: Design Flow
Place poles and zeros in transfer function
Compensate for digital phase margin erosion
Convert transfer function to z-domain
Convert z-domain to discrete time domain
Implement time-difference equation in code

## Slide 9: Compensation example
SMTR Voltage Compensation

## Slide 10: S to Z to N
Defense Ground & Airborne Systems 80%
Defense

## Slide 11: Recommendation
Buy piccolo prototype
  Piccolo controlSTICK - $39
  Piccolo USB Experimenter’s Kit - $79
Implement controller on forward topology
Compare performance with analog controller

## Slide 12: The Crane Advantage!
for more information please visit CraneAE.com